## Slide 1: 2022 Spec Training
Semi-Rigid Barriers

## Slide 2: What are semi-rigid barriers?
  Class A Beam Guard
  MGS Beam Guard
  Thrie Beam Transitions
  Thrie Beam Barrier
  End Treatments (Can act like beam guard in some impacts)
    EATs
    Type 2 New SDD in Aug 2021
    Thrie Beam Bullnose New in Aug SDD 2020
Long-Spans, Type K, LHW, Half and Quarter Post Spacing
Notes: Note that grading is important.
Steel post
Install hardware as detailed.

## Slide 3: Review the SDDs in your plan
What SDD is associated with the barrier installation?
    What SDDs are in the Plan?
      What version of the SDD are you using?
EAT SDD 14B44
MGS SDD 14B42
MGS Thrie Beam Approach SDD 14B45
SDD14B42 – 06a
Notes: Don’t mix and match SDDs

## Slide 4: Review the SDDs in your plan
  What post should be installed according to the SDD?
Part 2
These post are different than..
than these posts..

## Slide 5: Know the different post types.
Is this the correct post being installed?
  Material
    Wood
    Steel
  Type
    BCT
    CRT
    MwRSF Slip Post
    “Normal”
  Length
BCT
CRT
MwRSF Slip Post

## Slide 6: What is considered unacceptable?
Posts that are more than 3” short are not acceptable.
Posts that are too long are not acceptable.
Using the wrong type of post is not acceptable:
  Using a CRT post where “normal” post should be installed.
  Using steel posts where wood posts are needed.
Missing posts are not acceptable.
Mixing posts types and post spacing.

## Slide 7: What actions to take?
Install the correct posts.
If correct posts cannot be installed discuss with:
    Project Engineer
  If needed, discuss with Designer, or Construction Oversight Engineer
    Future designs can be improved.
    Construction Oversight Engineer may know how to handle these situations or call on central office staff for assistance.